## Slide 1
S. NO. | GENERAL PURPOSE COMPUTING SYSTEMS | EMBEDDED SYSTEM
1 | A combination of generic hardware and general purpose operating system for executing variety of applications | Combination of special purpose hardware and embedded OS for executing a specific set of application
3 | Applications can be modified by user | Firmware of the embedded system is pre- programmed and it is non-modifiable by the end user
4 | Performance is a key deciding factor in the selection of the system. Always “Faster is better”. | Application specific requirements (like performance, power, memory, cost) are key deciding factor
5 | Personal computer, Laptops | DVD player, Digital camera

## Slide 2
Microprocessor (µP)
Microcontroller (µC)
Feature
Designed for general-purpose computing applications
Designed for specific embedded system applications
Purpose
CPU with on-board memory, peripherals, and I/O interfaces
Single-chip computer system with on- board memory, peripherals, and I/O interfaces
Architecture
Higher cost+ power
Lower cost+ power
Cost & power
More flexible
Fixed instruction set
Instruction set
Harvard Architecture
Von Neuman Architecture

## Slide 3: Classification of μP
Micro Processors
General Purpose Processors (GPP)
Application Specific Processors
Digital Signal Processor (DSP)
Application Specific Integrated Circuit (ASIC)
Application Specific Instruction Set Processor (ASIP)
37

## Slide 4: Classification of μP General Purpose Processors (GPP)
perform multiple tasks
Pros - Flexible, easy to design, low cost, easy to reprogram
Cons - Poor performance, High power consumption
38
Classification of μP
Application Specific Processors (ASP)
Contains only the components needed to execute a single program
Pros – Good performance, less power consumption, good overall cost
Cons – difficult to design, high design cost, difficult to reprogram

## Slide 5
Feature | DSP (Digital Signal Processor) | ASIC (Application-Specific Integrated Circuit) | ASIP (Application-Specific Instruction Processor)
Overview | Specialized microprocessor for digital signal processing tasks and real time mathematical computations. | Custom-designed chip tailored for a specific application or task. Completely implemented in hardware. | Combines features of both DSP and ASIC, offering customizable hardware & instruction sets for specific tasks.
Advantages | Flexibility: Can be programmed for various applications. Real-time processing capability. Cost-effective for small volumes. | High performance: Optimized for specific tasks. Low power consumption – does only specific tasks | Programmable, like a DSP, but with specialized instructions. More flexible than ASIC, less than DSP. Custom instructions provide optimization.
Disadvantages | - Higher power consumption compared to ASICs. - Not as fast or efficient as ASICs. - Limited by general-purpose architecture. | Lack of flexibility: Cannot be reprogrammed for different tasks. functionality is hard-coded. - Expensive and time-consuming to design and manufacture. | Less efficient than ASICs for very specific tasks. Not as highly optimized as ASICs. More complex to design than DSPs. Higher cost than DSPs
Use Cases | Audio and video processing. Streaming platforms Telecommunications. Real-time data processing. | - High-volume, performance-critical applications. - Consumer electronics. - Networking devices. | - Custom applications requiring specific processing capabilities. - Embedded systems with specialized tasks.

## Slide 6: ES : Design Process
Consumer grade moving map for driving use
Power button; two control button
Back-lit LCD Display 400x600
Uses 5-receiver GPS system; three user-selectable resolutions; always displays current latitude and longitude
Updates screen within 0.25 seconds upon movement 100mW
30 USD
2” x 6” and 250 grams
1kg
Product Name GPS Navigation System
Purpose Inputs Outputs Functions
Performance Power
Cost
Size & Weight
59
Step 1: Requirements: Informal descriptions gathered from the customer are known as requirements

## Slide 7: ES : Design Process
Step 2: Specifications : serves as the contract between the customers and the architects.
  Specification would include details for several components:
    Data received from the GPS satellite
    Map data
    User interface
    Operations that must be performed to satisfy customer requests
    Background actions
60
Step 3: Architecture
  Specification describes only the functions of the system
  Implementation of the system is described by the Architecture
  Architecture is a plan for the overall structure of the system.
  It will be used later to design the components

## Slide 8: ES : Design Process

## Slide 9: ES : Design Process
Step 4: Hardware & Software Components
  In example GPS Reveiver
  In the moving map, GPS receiver is a predesigned standard hardware component.
  Topographic software is a standard software module which uses standard routines to access the database.
  Printed circuit board are the components which needs to be designed.
  When creating these embedded software modules, ensure the system runs properly in real time and that it does not take up more memory space than allowed.
65

## Slide 10: ES : Design Process
Step 5: System Integration
  After the components are built, they are integrated
  Bugs are typically found during the system integration
  By debugging a few modules at a time, simple bugs can be discovered
  By fixing the simple bugs early, more complex bugs can be discovered
  Appropriate debugging facilities during design which can help to ease system integration problems.
66

## Slide 11: ES : Design Process Example: Automatic Chocolate Vending Machine
68
Requirements
  Purpose:
    To sell chocolate through an ACVM from which children can
automatically purchase the chocolates.
    The payment is by inserting the coins into a coin-slot.
  Inputs:
    Coins of different denominations through a coin slot.
    User commands.
  Outputs:
    Chocolate and signal to the system that subtracts the cost from the
value of amount collected.
    Display of the menus for GUIs, time and date, advertisements, welcome and thank messages.

## Slide 12: ES : Design Process Example: Automatic Chocolate Vending Machine
69
Requirements
  A child sends commands to the system using a GUI.
    It must consists of the LCD display and keypad units.
The child inserts the coins for cost of chocolate and the machine delivers the chocolate.
If the coins are not inserted as per the cost of chocolate in reasonable
times then all coins are refunded.
If the coin amount more, the excess amount is refunded along with chocolate.
The coins for the chocolates purchased collect inside the machine in a collector channel, so that owner can get the money, again through appropriate commands using the GUI.
USB wireless modem enables communication through Internet to the ACVM owner.

## Slide 13: ES : Design Process Example: Automatic Chocolate Vending Machine
Design Metrics
  Power Dissipation: As required by mechanical units, display units and
computer system
  Performance: One chocolate in two minutes and 256 chocolates before next filling of chocolates into the machine.[Assumed]
  Process Deadlines: Machine waits for maximum 30 s for the coins and machine should deliver the chocolate within 60 s.
  User Interfaces: Graphic at LCD or touch screen display on LCD and commands by children or machine owner through fingers on keypad or touch screen
  Engineering Cost: US$ 50000 (assumed)
  Manufacturing Cost: US$ 1000 (assumed)

## Slide 14: ES : Design Process Example: Automatic Chocolate Vending Machine
Specifications
  Alphanumeric keypad on the top of the machine.
    A child interaction with it when buying a chocolate. Owner commands
and interaction with the machine.
  Three line LCD display unit on the top of the machine.
    Displays menus, entered text, pictograms, and welcome, thank and
other messages, and time and date.
    Child as well as the ACVM owner GUIs with the machine using keypad and display

## Slide 15: ES : Design Process Example: Automatic Chocolate Vending Machine
Specifications
  Coin insertion slot:
    So that the child can insert the coins to buy a chocolate.
  Delivery slot
    To collect the chocolate, and coins if refunded.
  Internet connection port
    So that owner can interact with ACVM from remote location.

## Slide 16: ES : Design Process Example: Automatic Chocolate Vending Machine
Specifications : Overall System Architecture

## Slide 17: ES : Design Process Example: Automatic Chocolate Vending Machine
Specifications : Hardware Design

## Slide 18: ES : Design Process Example: Automatic Chocolate Vending Machine
Specifications : Software Design

## Slide 19: ES : Design Process Example: Digital Camera
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
lens
Digital camera chip
CCD
Single-functioned -- always a digital camera
Tightly-constrained -- Low cost, low power, small, fast
Reactive and real-time -- only to a small extent

## Slide 20: ES : Design Process Example: Projector

## Slide 21: ES : Design Process Example: Digital Fan

## Slide 22: 8051 Architecture
88

## Slide 23: 8051 Architecture
90
CPU: monitors and controls all operations performed
Interrupt Control: Two external interrupts (INT0 & INT1), Two timer (TF0 & TF1) interrupts and One serial port (RI / TI) interrupt.
ROM: The memory which is used to store the program of Microcontroller, is known as code memory or Program memory.
RAM: The memory to store data or operands temporarily. This memory is known as Data Memory.
Bus Control: collection of wires which work as a communication channel or medium for transfer of Data. 2 Type of Buses:
  Address Bus: 16 bit address bus. It used to address memory locations.
  Data Bus: 8 bits data bus. It is used to carry data.
Crystal Oscillator: works as a clock source.
I/O Ports: 32 I/O pins arranged as four 8-bit ports (P0 - P3)

## Slide 24: PIC – Features
This powerful (200 nanosecond instruction execution) yet easy- to-program (RISC instructions).
PIC16F877A features
256 bytes of EEPROM data memory,
Self programming,
An ICD - In-Circuit Debugging
2 Comparators,
8 channels of 10-bit Analog-to- Digital (A/D) converter,
2 input capture/output
compare/PWM functions,
The synchronous serial port can be configured as either 3-wire Serial Peripheral Interface (SPI ) or the 2-wire Inter- Integrated Circuit (I²C ) bus and A Universal Asynchronous Receiver Transmitter (USART).

## Slide 25
EEPROM
Timer 3
Synchronous serial port
Asynchronous serial port
(UART)
10 bit ADC ports
Parallel slave port

## Slide 26
Special Functions of PIC16F877A I/O Pins
8 K ROM + 368 bytes RAM
“File Register” locations (8-bits wide) for temporary storage of data.
256 bytes nonvolatile EEROM for storage of calibration data, user-customized option settings, etc. Each of the 35 RISC instructions fits in just one location, permitting fast instruction execution time
Three hardware timers: Timer 0 (RA4/TOCK1 pin), Timer 1
(RC0/T1OSO/TICKI and RC1/T1OSI pins), and Timer 2 (no external pins are associated with this timer – this timer can be set to periodically interrupt via the PR2 period register).
10-bit, 8-channel analog-to-digital converter (analog inputs on Ports A and E)
8-bit parallel slave port (PSP) for making the PIC look like an addressable 8-bit peripheral register on a host computer’s bus.
  Port D for the 8-bit data bus connection and
  Port E for the RD\, WR\, and CS\ bus control lines).
Special Functions of PIC16F877A I/O Pins
Synchronous serial data port (SDA and SCL pins) used for implementing master and slave serial peripheral interface I2C serial interfaces.
Asynchronous serial data port (UART)

## Slide 27
 | 8051 | PIC | ARM
Bus width | 8-bit | 8/16/32-bit | 32/64-bit
Speed | 12 Clock/instruction cycle | 4 Clock/instruction cycle | 1 clock/ instruction cycle
ISA | CISC | Some feature of RISC | RISC
Memory Architecture | Von Neumann architecture | Harvard architecture | Modified Harvard architecture
Power Consumption | Average | Low | Low
Cost | Very Low | Average | Low

## Slide 28: ARM Architecture : Features

## Slide 29: ARM Core Dataflow Model

## Slide 30: ARM Core Dataflow Model
Instruction Decoder: It translates instructions before they are executed.
Register File: A storage bank made up of 32-bit registers.
Sign extend hardware: Converts signed 8-bit and 16-bit numbers to 32-bit values
Source Registers: two source registers, Rn & Rm, and a single result or destination register, Rd.
ALU & MAC:
  Takes the register values Rn and Rm from the A and B buses and computes result.
  Data processing instructions write the result in Rd directly
  Load and store instructions use the ALU to generate an address to be held in the address register.
Address Register & Incrementor: For load and store instructions the incrementor updates the address register before the core reads or writes the next register value from or to the next sequential memory location.
Barrel Shifter: Provides five types of shift - Logic Shift left (LSL), Logic Shift Right (LSR), Arithmetic Shift Right (ASR), Rotate Right(ROR), Rotate Right Extended (RRX). After passing through the functional units, the result in Rd is written back to the register file using the Result bus.

## Slide 31: ARM Processor : Modes
109
Each processor has mode:
  PRIVILEGED read-write access
  NONPRIVILEGED only read access

## Slide 32: ARM Processor : CPSR Register