## Slide 1: Building Process for Embedded Systems
In embedded software development, the build tools run on a host computer that differs from the target hardware platform.
Compiler, Assembler, Linker, Locator, Debugger
Produces executable binary image that will run on target embedded system
To develop software for an Embedded System
Create source file (on Host)
Compile/Assemble: translate into machine code (on Host)
Link: combine all object files and libraries, resolve all symbols (on Host)
Locate: assign memory addresses to code and data (on Host)
Download: copy executable image into Target processor memory
Execute: reset Target processor
1

## Slide 2
14
Compiler:
translate programs written in human-readable language into binary-object that contains set of machine-language instructions (opcodes) and data resulting from language translation.
Symbol table in the object file contains names and locations of all variables and functions referenced within the source file.
Linker:
Object files themselves are individually incomplete, some of the internal variable and function references not yet been resolved.
The job of the linker is to combine these object files and resolve all of the unresolved symbols and form a new complete relocatable object file.
the program is complete except for one thing: no memory addresses have yet been assigned to the code and data sections within.
Locator:
The locator assigns physical memory addresses to each of the code and data sections within the relocatable program and produces an output file that contains a binary memory image that can be loaded into the target.

## Slide 3: Build Procedure Arcom Viper-lite Development Board
COMPILE
The basic structure for the gcc compiler command is:
The command-line options we’ll need are:
-g
-c
-Wall
-I../include
To generate debugging info in default format
To compile and assemble but not link
To enable most warning messages
To look in the directory include for header files
Here are the actual commands for compiling:
So if all goes well, there will now be two additional object files — led.o and blink.o—in the working directory.

## Slide 4
GNU linker performs the linking and locating of the object files.
For locating, there is a linker script file named viperlite.ld that we input to ld in order to establish the location of each section in the Arcom board’s memory.
The structure for the linker and locater ld command is:
The command-line options we’ll need for this step are:
To generate a map file and use the given filename
To read the linker script
To set the text and data sections to be readable and writable
-Map blink.map
-T viperlite.ld
-N
-o blink.exe
To set the output filename (if this option is not included, will use the default output filename a.out)
The actual command for linking and locating is:
LINK AND LOCATE
The order of the object files determines their placement in memory.
Result of this command is the creation of two files— blink.map and blink.exe
Linker script and memory map section contains a breakdown of the memory contribution of each and every file that was linked into the final image.

## Slide 5: Loading on the Target
Two ways of downloading the binary image on the embedded system:
Using a Device Programmer:
  Step 1: Once the binary image is ready on the computer, the device programmer is connected to the computer.
  Step 2: Device programmer contains a software interface through which the user selects the target uP/uC for which the binary image has to be downloaded.
  Step 3: Device programmer then transfers the binary image bit by bit to the chip.
Using In System Programmer(ISP):
  Is the ability of programming the embedded processor/controller while it is installed in a complete system, rather than requiring the chip to be programmed prior to installing it into the system.
  Allows firmware updates to be delivered to the on-chip memory of microcontrollers and related processors without requiring specialist programming circuitry on the circuit board, and simplifies design work
  User through the ISP’s software interface sends the binary image to the target board.
  This avoids the requirement of frequently removing the microprocessor / microcontroller or ROM for downloading the code if a device programmer had to be used.

## Slide 6: Debugging Tools
SIMULATOR
Disadvantage - it only simulates the processor, and not the peripherals.
REMOTE DEBUGGER
It is used to monitor/control/download/execute and debug embedded SW over a comm. link.
The front-end of the GUI debuggers contain several windows to show the active part of the source code, current register contents, information about the executing program.
Backend provides low-level control of target processor, runs on target processor and communicates to the front-end over a communication link.
Debugger and software being debugged are executing on two different computer systems.
Disadvantage: inability to debug startup code, code must execute from RAM, requires a target processor to run the final software package
IN-CIRCUIT EMULATOR (ICE)
Emulation refers to the ability of a computer program or electronic device to imitate another program or device
Contains a copy of target processor, plus RAM, ROM, and its own embedded software.
It allows you to examine the state of the processor while the program is running.
ICE provides greater flexibility, ease for developing various applications on a single system in place of testing that multiple targeted systems.
Disadvantage of this method is that, it is expensive.

## Slide 7: DFG
Round nodes: Represents or denotes operators.
Square nodes: Represents values.
Advantages of DFG:
It orders the way operations can be performed in a program.

## Slide 8: Control DFG
Conditional Blocks in Control DFG:
if (cond1) basic_block_1( );
else basic_block_2();
basic_block_3( );
switch (test1) {
case c1: basic_block_4( ); break;
case c2: basic_block_5( ); break;
case c3: basic_block_6( ): break;
}
Building Loop in Control DFG:
while (a < b)
{
a = proc1(a,b);
b= proc2(a,b);
}
Constructs a model for decision and data flow of a program.
Consists of - decision nodes and edges labelled with possible outcomes

## Slide 9: Petri Net Model/ Place Transition Net Model
Interaction between asynchronous and concurrent processes. In asynchronous process, start and sequence of processes may vary during the execution
Petri Net(PN) is very similar to State Transition Diagrams which model the system behavior
COMPONENTS OF PETRINET MODEL
Places (circles) : possible states of the system;
Transitions (rectangles) : events which cause the changes of state (firing)
Arcs (arrows) : Every arc simply connects a place with a transition or a transition with a place.
Tokens(black dot): Change of state is denoted by a movement of token(s) from place(s) to place(s). Once firing is initiated, tokens will be transferred from input to output places

## Slide 10
Petri net with two places and one transaction.
Sequential Execution:
  Transition t2 can take place only after t1.
Concurrency:
  t1 and t2 are concurrent process
Merging:
  When several tokens are arrived at same transition merging will take place
Synchronization:
  Transition t1 will be enabled only when at least one token is available at each of its input places
p1: input place
p2: output place

## Slide 11
POS terminal generally does the following:
Validate the user using 4-digit PIN number
Checks whether the funds in a customer’s bank account are sufficient
Transfers the funds from the customer’s account to the seller’s account
Records the transaction and prints a receipt
Scenario 1: Normal: Enters all 4 digits and press OK.
Scenario 2: Exceptional: Enters only 3 or less digits and press OK
EXAMPLE – 1: POINT OF SALE (POS) MACHINE

## Slide 12
EXAMPLE – 2 : VENDING MACHINE
Machine dispenses two kinds of snack bars 20c and 15c.
Constraint: 10c and 5c coins can only be used
Scenario 1: Deposit four 5c, take 20c snack bar.
Scenario 2: Deposit 10 + 5c, take 15c snack bar.
Scenario 3: Deposit 5 + 10 + 5c, take 20c snack bar.

## Slide 13
EXAMPLE – 3 : ORDER MANAGEMENT IN A RESTAURANT
Scenario 1:
  Waiter takes order from customer 1
  Serves customer 1
  Takes order from customer 2
  Serves customer 2.
Scenario 2:
  Waiter takes order from customer 1
  Takes order from customer 2
  Serves customer 2
  Serves customer 1

## Slide 14: Unified Modelling Language
Use Case Diagram: Shows functional requirements and user interactions. Components: Actors, use cases, system boundary.
Class Diagram: Represents the static structure of the system architecture(classes, attributes, relationships). Components: Classes, attributes, methods, associations.
Sequence Diagram: Illustrates object interactions in a time sequence and operation flow. Components: Objects, lifelines, messages, activations.
State Diagram: Shows object states and transitions due to events. Components: States, transitions, events, initial/final states.
Activity Diagram: Depicts the flow of activities and control flow. Components: Activities, control flows, decision points.
Sequence, state and activity diagram
System Requirement
System Structure
System
characteristics
Use case diagrams
Class diagram

## Slide 15: USE CASE DIAGRAM
Shows different ways a user can interact with the system. Extensibility makes UML more powerful and flexible.
Dependency: Relationship between two elements of a system
Association: describes how the elements are associated. The multiplicity (1, *, etc.) to show how many objects are associated
Generalization: inheritance relationship / parent-child relationship
Dependent
Independent

## Slide 16: Example: ATM System
UML

## Slide 17: Example: Washing Machine
UML

## Slide 18: Class Diagram
Set of interrelated classes
Collection of classes, interfaces, associations, collaborations and constraints.
Classes can be “is-a” or "has-a" relationship
Attributes
Methods
Student
+ name: String #Roll: Int -Section: String
+ display () -Add () -Edit () # Delete ()
Class
Visibility
+ Public
- Private
# protected
Inheritance
Anil |  | 
Sunil
Association
Aggregation
Relationships

## Slide 19: ATM - Diagram

## Slide 20
Elevator – Class Diagram

## Slide 21: Class Diagram Example Washing Machine

## Slide 22: Sequence Diagram
Interactions among the different elements in the model
Describes the dynamic behavior of the system
It emphasizes on the time sequence of messages
Used in planning and understanding the functionality of existing and future scenario
Lifeline Notation
Activation Bar
Synchronous message
Return message
Alt | 
If it is valid | 
Else | 
Object
Alternate frame

## Slide 23
ELEVATOR SYSTEM
Sequence Diagram

## Slide 24
Sequence Diagram
Vending Machine

## Slide 25: State Diagram
State diagram stores the status of object
It’s a
behavioral diagram
It explains the dynamic behavior of a class
State diagrams an be used to understand the reaction of
objects on receiving external stimuli
Initial state
Transition Symbol
State
Composite State
Self Transition
Final state

## Slide 26: State Diagram
Idle
Send order request
Special or Normal order
Order confirmation
Dispatch order
Initial state
Final state
Transition
Abnormal exit state
ONLINE ORDER MANAGEMENT

## Slide 27: State Diagram
ATM machine

## Slide 28: State Diagram
"User" Behavior for Elevator System”
“Elevator Control System"

## Slide 29: Activity Diagram
Activity
Action
Control flow
Object flow
Initial node
Final node
Object node
Decision node
Merge node
Fork node
Join node
Behavioral diagram
Shows the control flow from start to finish point including other decisions paths that is being executed
It can explain both sequential and concurrent processing

## Slide 30: Activity Diagram
Activity Diagram of an Order Management System
Customer sends an order request
Order request system
confirms the order
Confirm order
Dispatch order
Start of process
Termination
[Yes]
[No]
Condition check
[Yes]
[No]

## Slide 31: Activity Diagram Elevator
ELC – Elevator Logic Control ERS – Elevator Request Service

## Slide 32: Activity Diagram Vending Machine

## Slide 41: LOGIC ANALYZER
The main elements of a logic analyzer are probes, internal clock generator, threshold generator, comparator, memory, trigger block. Appropriate probes are used to connect the data lines of a digital system (i.e., System Under Test (SUT)) to the logic analyzer. The internal clock generator generates the clock pulses which are used for sampling the input data, The comparator block compares the sampled data and a specified threshold voltage generated by threshold generator. The memory of the logic analyzer is used to store the data captured by logic analyzer.

## Slide 42: WORKING OF LOGIC ANALYZER
After receiving the signal from the SUT, it samples the input signal at certain clock frequency.
In the sampling process, it compares the input signal with a certain threshold voltage at each sample point and depending upon the result of comparison it converts the input signal at that sampling instant into a logic 1 (High) or logic 0 (low) state.
Thus, by sampling process the input signal gets converted into a pattern of 0’s and l’s.
The sampled data is then stored in the memory of logic analyzer
with each sample point occupying a single memory location.
Types of Logic Analysers:
Logic Timing Analyzer (Asynchronous Measurements)
This Analyzer “samples” the waveform at each edge of the internal clock generated at regular intervals of time stores them in memory and displays the same in a timing waveform. This is called as “asynchronous” measurement since the internal clock runs asynchronous to the logic system being tested.

## Slide 43: 2) Logic Analyzer (Synchronous Measurement)
This uses a signal from the circuit under test, external clock determines when the logic signal is to be stored. This is called as “synchronous” measurement since the external clock runs synchronous to the logic system being tested. Modern logic analyzer combines both the above functions in one unit.
The Fig. 1. shows block diagram of a logic analyzer. It combines both functions i.e., asychronous and synchronous. The logic signal data to be measured enters the Analyzer through “Probe Buffer”. The output from the buffer is clocked into a latch at regular intervals. The latched data is stored in the memory and is displayed by the microprocessor (µP).
The signal data used to latch can be obtained from two different sources. For asynchronous operation an internal clock is used and for synchronous operation, an external clock is used.

## Slide 44: Applications of Logic Analyzer
A logic analyzer has the ability to capture and display the data of multiple digital signals (usually more than eight) at a time. Hence, a logic analyzer can be used to examine a large number of digital signal lines of a digital system.
Note: The logic probe can view only one signal at a time and also it cannot store it. When it is required to have a record of more than one signal simultaneously e.g., when it is necessary to look at the logic levels of all the lines of a microprocessor bus, we use a “logic Analyzer”.
Characteristics:
Multiple channels
Provide a time display of logic states
Does not display analog information